## Slide 1: Reference Architecture
BLE Device
Web App
Web Browser, Smartphone App
BR
Android Device
Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Border Router

## Slide 2: Protocol Layers and IoT Standards
Application Software
IPSO Objects
OMA LWM2M
CoAP
HTTP
6LowPAN
IPV4/IPV6
MCU – 16KiB RAM
MPU
802.15.4
WiFi, Ethernet
Hardware
HW Network
Routing
Application Protocol
API
Data Models
Application

## Slide 3: Protocol Layers Work Together
IPSO Smart Objects are based on OMA LWM2M
  Defines application objects composed of resources using the LWM2M Object Model
  Complex objects can be composed from simple objects
  Easy to add new resource and object types as needed
OMA LWM2M is based on CoAP
  Provides a server profile for IoT middleware
  Defines a simple reusable object model
  Defines management objects and reuses REST API for onboarding and device life cycle management
CoAP and related standards from IETF
  CoAP Protocol (RFC 7252) provides a REST API for device abstraction and data compatibility layer for constrained networks and devices
  HTTP Proxy provides application abstraction through standard web APIs
  Core-link-format (RFC 6690) provides a way to add semantic descriptors in the form of web links and enables local resource discovery through the REST API
  Resource Directory provides an API for scalable discovery and linking using core-link-format primitives

## Slide 4: Internet of Things
CoAP Protocol

## Slide 5: CoAP is REST for Constrained Devices
Makes each device a lightweight server that exposes a REST API
A CoAP device can be both client and server
Roles can be reversed and the sensor, as a client, can update a REST API at another node, device or server

## Slide 6: CoAP Use Case Requirements
REST API
Less Constrained
Resource Constrained

## Slide 7: Transport Model
Transport
  CoAP currently defines:
  UDP binding with DTLS security
  CoAP over SMS or TCP possible
Base Messaging
  Simple message exchange between endpoints
  Confirmable or Non-Confirmable Message
  Answered by Acknowledgement or Reset Message
REST Semantics
  REST Request/Response mapped onto CoAP Messages
  Method, Response Code and Options (URI, content-type etc.) define REST exchanges, very similar to HTTP (HTTP 404 response semantics (not found) mapped to CoAP 4.04 response code)
Asynchronous Notifications
  Observer option for GET allows asynchronous state update responses from a single request

## Slide 8: CoAP Header – Binary Protocol Mapping

## Slide 9: CoAP Request - Response
Response with Data Payload
Confirmable Request

## Slide 10: CoAP Caching
CoAP includes a simple caching model
  Cacheability determined by response code
  An option number mask determines if it is a cache key
  Resource Discovery returns links to cache/proxy
Freshness model
  Max-Age option indicates cache lifetime
Validation model
  Validity checked using the Etag Option
A proxy often supports caching
  Usually on behalf of a constrained node,
  a sleeping node, a node behind a firewall,
  or to reduce network load and battery drain

## Slide 11: CoAP Proxy Caching

## Slide 12: CoAP Observe – Asynchronous Notification
See draft-ietf-core-observe

## Slide 13: Internet of Things
CoAP Semantic Links & Discovery

## Slide 14: Discovery
Service Discovery
  What services are available in the first place?
  Goal of finding the IP address, port and protocol
  Can be performed by e.g. DNS-SD when DNS is available
  CoAP Services can be discovered using Resource Discovery
Resource Discovery
  What are the Web resources I am interested in?
  Goal of finding URLs to link into applications
  Performed using Web Linking and REST API
    CoRE Link Format is designed to enable resource discovery

## Slide 15: Web Linking for Machines
RFC6690 is aimed at Resource Discovery for M2M
  Defines semantic link serialization and content-types suitable for M2M
  Defines a well-known resource where links are stored
  Enables query string parameters for discovery by attribute and relation
  Can be used with unicast or multicast (CoAP)
Resource Discovery with RFC6690
  Discovering the links hosted by CoAP (or HTTP) servers
  GET /.well-known/core?optional_query_string
  Returns a link-format document
  URL, resource type, interface type, content-type, size are some basic relations

## Slide 16: Local Network Discovery
Could return a link-format document:
</3//9>;obs;rt=“urn:X-ipso:batt-level”;ct=”50”,
</3//0>;rt=”urn:X-ipso:dev-mdl”;ct=”50”,
</3//1>;rt=”urn:X-ipso:dev-mfg”;ct=”50”,
</3305/0/5800>;obs;rt=”urn:X-ipso:pwr-w”;ct=”50”,
</3305/0/5805>;obs;rt=”urn:X-ipso:pwr-accum-wh”;ct=”50”,
</3303/0/5700>;obs;rt=”urn:X-ipso:temp-C”;ct=”50”
CoAP Server
CoAP Client
DISCOVERY
GET /.well-known/core
2.05 Content
Could use multicast

## Slide 17: Resource Directory Discovery
See draft-ietf-core-resource-directory
Web Applications Discover
Registered Resources
CoRE Link Format defines
  The link format
  Peer-to-peer discovery
A directory approach is also useful
  Supports sleeping nodes
  No multicast traffic, longer battery life
  Remote lookup, hierarchical and federated distribution
CoRE Link Format is used in Resource Directories
  Nodes POST (register) their link-format to an RD
  Nodes PUT (refresh) to the RD periodically
  Nodes may POST to add links to the RD
  Nodes may DELETE (remove) their RD entry
  Nodes may GET (lookup) the resources of other nodes

## Slide 18: Resource Directory
See draft-ietf-core-resource-directory
core.rd service
REGISTRATION
POST /rd?ep=‘235598376’&lt=19999
</3303/0/5700>;rt=“urn:X-ipso:temp-C”
Endpoint
2.01 Created Location:/rd/235598376
DISCOVERY
GET /rd-lookup?ep&rt=“urn:X-ipso:temp-C”
2.05 Content
</235598376/3303/0/5700>;rt=“urn:X-ipso:temp-C”
Endpoint

## Slide 19: Internet of Things
OMA LWM2M

## Slide 20: LWM2M Architecture
Web Applications
  Application abstraction through REST API
  Resource Discovery and Linking
LWM2M Clients are Devices
  Device abstraction through CoAP
  LWM2M Clients can be CoAP Servers
  Any IP network connection
LWM2M Server
  CoAP
  HTTP Caching Proxy
  Resource Directory
  Gateway and Cloud deployable

## Slide 21: LWM2M Interfaces
Bootstrap Interface
  Configure Servers & Keying
  Pre-Configure, Smart Card, Server Initiated Bootstrap
Registration Interface
  RFC6690 and Resource Directory
Management Interface Using Objects
  Management Objects and Resources
  Uses the CoAP REST API
Reporting Interface
  Subscription to Object Instances and Resources
  Asynchronous notification using CoAP

## Slide 22: LWM2M Object Model
A Client has one or more Object Instances
An Object is a collection of Resources
A Resource is an atomic piece of information that can be
  Read, Written or Executed
Resources can have multiple instances
Objects and Resources are identified by a 16-bit Integer, Instances by an 8-bit Integer
Objects/Resources are accessed with simple URIs:
/{Object ID}/{Object Instance}/{Resource ID}
Ex: /3/0/1 (Object Type=Device, Instance=0, Resource=Device Mfg.)

## Slide 23: LWM2M Management Objects

## Slide 24: Example Object – Position Object

## Slide 25: Internet of Things
IPSO Smart Objects

## Slide 26: IPSO Alliance
IPSO Alliance - semiconductor, device, and system manufacturers
Smart Object Committee meets every 2 weeks, recently completed the Smart Objects 1.0 IPSO Technical Guideline
Uses the OMA LWM2M Object Model to define application objects
Resource IDs and Object IDs are registered with the OMNA
Provides a framework for Application Level Interoperability
Builds common definitions of web objects for use with standard web protocols (CoAP, HTTP)
Defines reusable resources and objects that map to physical sensors, actuators, objects

## Slide 27: IPSO Smart Objects
IPSO Smart Objects provide a common data model across different sensor types, enabling application level interoperability
Interoperability between end devices and applications
Allows decoupling of devices from dedicated application services
Repurposing and multi-purposing of devices, reusability of application software
Interoperability across platforms and M2M protocols
Enables developers of embedded device and web services to focus on the value endpoints

## Slide 28: IPSO Smart Object
Common representations and units
Refers to well-known namespaces like ucum
Default units e.g. Celsius, kPa
Object, object instances, and resource instances are addressable using paths constructed from object and resource type IDs
Example: GET /sensors/3303/0/5700
Returns a representation of the current value of the ‘5700’ resource (Current Value) from instance ‘0’ of Object Type ‘3303’ (Temperature)

## Slide 29: Example Smart Object - Temperature
Object with
Internal
resources

## Slide 30: Object Annotation
Semantic annotation (not part of LWM2M Standard) uses core-link-format metadata for semantic description
Described in IETF CoRE Interfaces document (http://datatracker.ietf.org/doc/draft-ietf-core-interfaces) enables GET by relation and attribute
  For example, GET /rd-lookup?ep&rt=“urn:X-ipso:temp-C”
  Returns: </sensors/3303/0/5700>;obs;if=“urn:X-ipso:sensor”;rt=“urn:X-ipso:temp-C”;ct=50;u=“ucum:degC”
Refers to qualified, resolvable namespaces and concepts
Supports CoRE Resource Discovery

## Slide 31: Example Smart Obejct Ad-Hoc binding

## Slide 32: Binding to Smart Thermostat

## Slide 33: Smart Object Summary
Simple web objects that represent common sensors, actuators, and data elements exposed for Internet of Things applications
Based on Internet and Industry Standards
Objects can be composed into more complex objects; for example a temperature object, set point object, and load control object can be combined to create a thermostat object
About to publish the first set of objects to cover some common Smart Home and Sensor use cases
New objects are easy to create; we are planning a developer-friendly process for creating and registering new objects

## Slide 34: Layered Standards
Application Software
IPSO Smart Objects
OMA LWM2M
CoAP
REST protocol for constrained devices
IETF Standard (RFC 7252)
Uses TCP or UDP, any IP connection
Discovery using IP Multicast or Directory
Service Layer Specification
Device Management over CoAP
Object Model for DM and Applications
Application Level Interoperability
Reusable Device to Application API
Not tied to any specific protocol
Not tied to specific device or protocol
Any Programming Language
Runs on devices, gateways, and services

## Slide 35: Standards References
IPSO Smart Object Guideline
  http://www.ipso-alliance.org/technical-information/ipso-guidelines
OMA LWM2M Specification
  http://openmobilealliance.hs-sites.com/lightweight-m2m-specification-from-oma
IETF CoAP and Related Specifications
  CoAP (RFC 7252):
  http://tools.ietf.org/html/rfc7252
  CoRE Link-Format (RFC 6690):
  http://tools.ietf.org/html/rfc6690
  CoRE Resource Directory: http://tools.ietf.org/html/draft-ietf-core-resource-directory-01
CoAP Community Site
  http://coap.technology/

## Slide 36: Internet of Things
OMA LWM2M and ARM mbed

## Slide 37: mbed Mapping to Reference Architecture
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
BLE Border Router
Web App

## Slide 38: Registration
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
REGISTER
REGISTER
REGISTER

## Slide 39: Discovery
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
DISCOVER
DISCOVER
DISCOVER

## Slide 40: Example Transaction
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
1. GET
3. REPLY
2. GET
4. REPLY

## Slide 41: Asynchronous Notification
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
NOTIFY
NOTIFY

## Slide 42: CoAP over BLE
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Border Router
Web App
GET
REPLY
GET
GET
REPLY
REPLY