## Slide 1: Reference Architecture
BLE Device
Web App
Web Browser, Smartphone App
BR
Android Device
Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Border Router

## Slide 2: Protocol Layers and IoT Standards
Application Software
IPSO Objects
OMA LWM2M
CoAP
HTTP
6LowPAN
IPV4/IPV6
MCU – 16KiB RAM
MPU
802.15.4
WiFi, Ethernet
Hardware
HW Network
Routing
Application Protocol
API
Data Models
Application

## Slide 3: mbed Mapping to Reference Architecture
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
BLE Border Router
Web App

## Slide 4: Registration
Android Device
http/REST
CoAP
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Web App
REGISTER
REGISTER

## Slide 5: Discovery
mbed
Device Server
http/REST
CoAP
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Web App
DISCOVER
DISCOVER

## Slide 6: Example Transaction
mbed
Device Server
http/REST
CoAP
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Web App
1. GET/PUT
3. REPLY
2. GET/PUT
4. REPLY

## Slide 7: Asynchronous Notification
mbed
Device Server
http/REST
CoAP
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Web App
NOTIFY
NOTIFY

## Slide 8: Device Server API – Endpoint Discovery
Endpoints can be discovered using the Device Server discovery interface
Endpoint discovery returns a JSON array of endpoint objects
http://10.10.10.10:8080/my_domain/endpoints
Device Server Endpoint Discovery URL
Domain Name

## Slide 9: Device Server API – Endpoint Discovery
GET http://10.10.10.10:8080/my_domain/endpoints
0: {
name: "MBED-061590140030"
type: "LWM2M test client"
status: "ACTIVE"
}-
1: {
name: "mbed-6230600c000f"
type: "mbed_device"
status: "ACTIVE"
}

## Slide 10: Device Server API – Resource Discovery
Resources can be discovered using the Device Server discovery interface
Resource discovery returns a JSON array of resource objects
http://10.10.10.10:8080/my_domain/endpoints/my_ep_name
Device Server Resource Discovery URL
Domain Name
Endpoint Name

## Slide 11: Device Server API – Resource Discovery
GET http://10.10.10.10:8080/my_domain/endpoints/my_ep_name
0: {
uri: "/3304/0/5700"
rt: "urn:X-ipso:humidity"
obs: false
type: ""
}-
1: {
uri: "/3303/0/5700"
rt: "urn:X-ipso:temperature"
obs: false
type: ""
}-
2: {
uri: "/3302/0/5500"
rt: "urn:X-ipso:presence"
obs: true
type: ""
}-

## Slide 12: Device Server API – Resource URL
Web API URLs are constructed from the resource URIs registered by the device, the endpoint name of the registered device, and a preconfigured domain name
http://10.10.10.10:8080/my_domain/endpoints/my_ep_name/3303/0/5700
Object ID, defines object type
Object Instance, one or more
Resource ID, defines resource type
Device Server Resource URL
Endpoint Name
Domain Name

## Slide 13: Device Server API – Resource URL
GET http://10.10.10.10:8080/my_domain/endpoints/my_ep_name/3303/0/5700
Returns -> 71.2

## Slide 14: Web Application Server
Web App Server
Server
http/REST
CoAP
Soft Endpoints
IP Device
IP Device
IP Device

## Slide 15: Web Application Server
The Device Server has REST interfaces for resource discovery, resource access, and asynchronous notification
Web Application Server runs an application that interacts with the device through the Device Server interfaces
Application server can run on it’s own instance or node, and connect to the device server over the network
Applications can be programmed in web-friendly languages like Python, Nodejs, Ruby
This example will focus on nodejs and Node-RED

## Slide 16: Application Server Setup
Each team will have a dedicated application server instance available – see the lab notes for details
Sign up on the Rackspace “iwantaserver” page and get your server’s IP address and root login
Follow the instructions in the lab note for setting up the server environment and Node-RED
Test the demo application with your mbed board running the LED Demo project

## Slide 17: Node-RED
Node-RED is a visual programming system based on node.js
Drag and drop programming using pre-configured and custom function nodes
Event driven data flow programming paradigm with MQTT-style messages consisting of a topic and a payload
Built-in nodes for HTTP, MQTT, JSON templates, and many other useful functions
A Node-RED Flow is a collection of nodes linked together

## Slide 18: Node-RED Demo Example Flow
Inject node creates a node-red message with a pre defined payload
http request node builds a request using the injected payload and sends it to a server
Debug node reports the http response from the server
(Device Server)

## Slide 19: Node-RED Configuration

## Slide 20: References
IPSO Smart Object Guideline
  http://www.ipso-alliance.org/technical-information/ipso-guidelines
Node-RED
  http://nodered.org/
mbed Device Server API reference (User Guide)
  https://github.com/connectIOT/SpringIotCourse/blob/master/Documents/NanoService_Platform_UserGuide.pdf
Some live examples of mbed Device Server and Node-RED, also MQTT
  http://smartobjectservice.com:1880/