## Slide 1: Reference Architecture
BLE Device
Web App
Web Browser, Smartphone App
BR
Android Device
Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
Border Router

## Slide 2: Protocol Layers and IoT Standards
Application Software
IPSO Objects
OMA LWM2M
CoAP
HTTP
6LowPAN
IPV4/IPV6
MCU – 16KiB RAM
MPU
802.15.4
WiFi, Ethernet
Hardware
HW Network
Routing
Application Protocol
API
Data Models
Application

## Slide 3: CoAP is REST for Constrained Devices
Makes each device a lightweight server that exposes a REST API
A CoAP device can be both client and server
Roles can be reversed and the sensor, as a client, can update a REST API at another node, device or server

## Slide 4: CoAP Request - Response
Response with Data Payload
Confirmable Request

## Slide 5: CoAP Observe – Asynchronous Notification
See draft-ietf-core-observe

## Slide 6: mbed Mapping to Reference Architecture
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
BLE Border Router
Web App

## Slide 7: Registration
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
REGISTER
REGISTER
REGISTER

## Slide 8: Discovery
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
DISCOVER
DISCOVER
DISCOVER

## Slide 9: Example Transaction
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
1. GET
3. REPLY
2. GET
4. REPLY

## Slide 10: Asynchronous Notification
BLE Device
Web Browser, Smartphone App
BR
Android Device
mbed
Device Server
http
http/REST
CoAP
BLE
Soft Endpoints
IP Device
IP Device
HW Device Endpoints
mbed OS
Web App
NOTIFY
NOTIFY

## Slide 11: Resources and Data Models
Web App
Device Server
HTTP
CoAP
IP Device
Resource:
An addressable element of a REST API
Has a path or URI
May represent a sensor or actuator
Has a set of operations e.g. GET, PUT
Exposed by devices, registered with server
Consumed by applications through server
The Data Model defines:
How the path is constructed - URI template
Which operations are allowed
Other properties like data type
Resources
Sensors

## Slide 12: Smart Object Data Model - Temperature
Object with
Internal
resources

## Slide 13: Smart Object Resource Design
Objects represent single points of interest, for example a temperature senor
An object may have multiple instances
Resources represent attributes of the object, for example the last measured value, the smallest measured value, the greatest measured value
Object and resource IDs are meant to be reusable, representing common measurements and concepts
Please see the IPSO Smart Object Guideline
3303/0/5700
Object ID, defines object type
Object Instance, one or more
Resource ID, defines resource type
Smart Object Data Model URI

## Slide 14: Smart Object Starter Pack

## Slide 15: Device Programming for Resources
The mbed library for LWM2M and Smart Objects provides resource classes (e.g. DynamicResource)
Two files are involved in resource programming
Resources are implemented in a <resource>.h file for each addressable resource, which is a wrapper for the generic class constructor and resource-specific code
Resources are configured and created in the main program (e.g. main.cpp)
Resources are registered with the Device Server when the endpoint start() is called, usually in main.cpp

## Slide 16: Device Programming for Resources
Refer to the lab note on resource programming for specific instructions
Some attributes and parameters need to be customized for each device
  Endpoint Name
  Registration Domain
  Device Server IP address
And for each resource
  Resource.h file
  Resource path
  Max-age to control cache lifetime - optional
  Observation sample time - optional

## Slide 17: Device Server API
Devices register resources with a Device Server by uploading links
Registrations have a lifetime and are refreshed periodically by the device
The Device Server is a proxy for resources that are registered by devices
Applications can access device resources by using the HTTP proxy, which exposes a web style REST API
Each registered device resource has a corresponding web API resource
Refer to the mbed Device Server User Guide

## Slide 18: Device Server API – Endpoint Discovery
Endpoints can be discovered using the Device Server discovery interface
Endpoint discovery returns a JSON array of endpoint objects
http://10.10.10.10:8080/my_domain/endpoints
Device Server Endpoint Discovery URL
Domain Name

## Slide 19: Device Server API – Endpoint Discovery
GET http://10.10.10.10:8080/my_domain/endpoints
0: {
name: "MBED-061590140030"
type: "LWM2M test client"
status: "ACTIVE"
}-
1: {
name: "mbed-6230600c000f"
type: "mbed_device"
status: "ACTIVE"
}

## Slide 20: Device Server API – Resource Discovery
Resources can be discovered using the Device Server discovery interface
Resource discovery returns a JSON array of resource objects
http://10.10.10.10:8080/my_domain/endpoints/my_ep_name
Device Server Resource Discovery URL
Domain Name
Endpoint Name

## Slide 21: Device Server API – Resource Discovery
GET http://10.10.10.10:8080/my_domain/endpoints/my_ep_name
0: {
uri: "/3304/0/5700"
rt: "urn:X-ipso:humidity"
obs: false
type: ""
}-
1: {
uri: "/3303/0/5700"
rt: "urn:X-ipso:temperature"
obs: false
type: ""
}-
2: {
uri: "/3302/0/5500"
rt: "urn:X-ipso:presence"
obs: true
type: ""
}-

## Slide 22: Device Server API – Resource URL
Web API URLs are constructed from the resource URIs registered by the device, the endpoint name of the registered device, and a preconfigured domain name
http://10.10.10.10:8080/my_domain/endpoints/my_ep_name/3303/0/5700
Object ID, defines object type
Object Instance, one or more
Resource ID, defines resource type
Device Server Resource URL
Endpoint Name
Domain Name

## Slide 23: Device Server API – Resource URL
GET http://10.10.10.10:8080/my_domain/endpoints/my_ep_name/3303/0/5700
Returns -> 71.2

## Slide 24: Standards References
IPSO Smart Object Guideline
  http://www.ipso-alliance.org/technical-information/ipso-guidelines
OMA LWM2M Specification
  http://openmobilealliance.hs-sites.com/lightweight-m2m-specification-from-oma
IETF CoAP and Related Specifications
  CoAP (RFC 7252):
  http://tools.ietf.org/html/rfc7252
  CoRE Link-Format (RFC 6690):
  http://tools.ietf.org/html/rfc6690
  CoRE Resource Directory: http://tools.ietf.org/html/draft-ietf-core-resource-directory-01
CoAP Community Site
  http://coap.technology/